## Slide 1
Computer Networking: A Top Down Approach
A note on the use of these Powerpoint slides:
We’re making these slides freely available to all (faculty, students, readers). They’re in PowerPoint form so you see the animations; and can add, modify, and delete slides (including this one) and slide content to suit your needs. They obviously represent a lot of work on our part. In return for use, we only ask the following:
If you use these slides (e.g., in a class) that you mention their source (after all, we’d like people to use our book!)
If you post any slides on a www site, that you note that they are adapted from (or perhaps identical to) our slides, and note our copyright of this material.
Thanks and enjoy! JFK/KWR
All material copyright 1996-2016
J.F Kurose and K.W. Ross, All Rights Reserved
7th edition Jim Kurose, Keith Ross Pearson/Addison Wesley April 2016
Chapter 3 Transport Layer

## Slide 2: Chapter 3: Transport Layer
our goals:
understand principles behind transport layer services:
  multiplexing（多路复用）, demultiplexing（多路分解）
  reliable data transfer
  flow control（流量控制）
  congestion control（拥塞控制）
learn about Internet transport layer protocols:
  UDP: connectionless transport （无连接的传输）
  TCP: connection-oriented reliable transport （面向连接的可靠传输）
  TCP congestion control

## Slide 3: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing（多路复用） and demultiplexing（多路分解）
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 4: Transport services and protocols
provide logical communication between app processes running on different hosts
transport protocols run in end systems
  send side: breaks app messages into segments（报文段）, passes to network layer
  rcv side: reassembles segments into messages, passes to app layer
more than one transport protocol available to apps
  Internet: TCP and UDP
application
transport
network
data link
physical
logical end-end transport
application
transport
network
data link
physical

## Slide 5: Transport vs. network layer
network layer: logical communication between hosts
transport layer: logical communication between processes
  relies on, enhances, network layer services
12 kids in Ann’s house sending letters to 12 kids in Bill’s house:
hosts = houses
processes = kids
app messages = letters in envelopes
transport protocol = Ann and Bill who demux to in-house siblings
network-layer protocol = postal service
household analogy:

## Slide 6: 传输层的作用是什么？
有哪些功能
分别跟协议栈中的哪几层有关联，提供什么服务？

## Slide 7: Internet transport-layer protocols
reliable, in-order delivery (TCP)
  congestion（拥塞） control
  flow（流量） control
  connection setup
unreliable, unordered delivery: UDP
  no-frills extension of “best-effort” IP
services not available:
  delay guarantees
  bandwidth guarantees
application
transport
network
data link
physical
application
transport
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
network
data link
physical
logical end-end transport

## Slide 8: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 9: Multiplexing/demultiplexing（多路复用和多路分解）
process
socket
use header info to deliver
received segments to correct
socket
demultiplexing at receiver:
handle data from multiple
sockets, add transport header (later used for demultiplexing)
multiplexing at sender:
transport
application
physical
link
network
P2
P1
transport
application
physical
link
network
P4
transport
application
physical
link
network
P3
Notes: 一般用到的是1~65535。
其中0不使用，1-1023为系统端口，也叫BSD保留端口。
0-1023： BSD保留端口，也叫系统端口，这些端口只有系统特许的进程才能使用；
1024~65535为用户端口，又分为：BSD临时端口(1024-5000)和BSD服务器(非特权)端口(5001-65535)。其中：
1024-5000： BSD临时端口，一般的应用程序使用1024到4999来进行通讯；
5001-65535：BSD服务器(非特权)端口，用来给用户自定义端口。

## Slide 10: How demultiplexing works
host receives IP datagrams
  each datagram has source IP address, destination IP address
  each datagram carries one transport-layer segment
  each segment has source, destination port number
host uses IP addresses & port numbers to direct segment to appropriate socket
source port #
dest port #
32 bits
application
data
(payload)
other header fields
TCP/UDP segment format

## Slide 11: Connectionless demultiplexing
recall: created socket has host-local port #:
DatagramSocket mySocket1 = new DatagramSocket(12534);
when host receives UDP segment:
  checks destination port # in segment
  directs UDP segment to socket with that port #
recall: when creating datagram to send into UDP socket, must specify
  destination IP address
  destination port #
IP datagrams with same dest. port #, but different source IP addresses and/or source port numbers will be directed to same socket at dest

## Slide 12: Connectionless demux: example
DatagramSocket serverSocket = new DatagramSocket
(6428);
transport
application
physical
link
network
P3
transport
application
physical
link
network
P1
transport
application
physical
link
network
P4
DatagramSocket mySocket1 = new DatagramSocket (5775);
DatagramSocket mySocket2 = new DatagramSocket
(9157);
source port: 9157
dest port: 6428
source port: 6428
dest port: 9157
source port: ?
dest port: ?
source port: ?
dest port: ?

## Slide 13: Connection-oriented demux
TCP socket identified by 4-tuple:
  source IP address
  source port number
  dest IP address
  dest port number
demux: receiver uses all four values to direct segment to appropriate socket
server host may support many simultaneous TCP sockets:
  each socket identified by its own 4-tuple
web servers have different sockets for each connecting client
  non-persistent HTTP will have different socket for each request

## Slide 14: Connection-oriented demux: example
transport
application
physical
link
network
P3
transport
application
physical
link
P4
transport
application
physical
link
network
P2
source IP,port: A,9157
dest IP, port: B,80
source IP,port: B,80
dest IP,port: A,9157
host: IP address A
host: IP address C
network
P6
P5
P3
source IP,port: C,5775
dest IP,port: B,80
source IP,port: C,9157
dest IP,port: B,80
three segments, all destined to IP address: B,
dest port: 80 are demultiplexed to different sockets
server: IP address B

## Slide 15: Connection-oriented demux: example
transport
application
physical
link
network
P3
transport
application
physical
link
transport
application
physical
link
network
P2
source IP,port: A,9157
dest IP, port: B,80
source IP,port: B,80
dest IP,port: A,9157
host: IP address A
host: IP address C
server: IP address B
network
P3
source IP,port: C,5775
dest IP,port: B,80
source IP,port: C,9157
dest IP,port: B,80
P4
threaded server

## Slide 16: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 17: UDP: User Datagram Protocol [RFC 768]
“no frills,” “bare bones” Internet transport protocol
“best effort” service, UDP segments may be:
  lost
  delivered out-of-order to app
connectionless:
  no handshaking between UDP sender, receiver
  each UDP segment handled independently of others
UDP use:
  streaming multimedia apps (loss tolerant, rate sensitive)
  DNS
  SNMP（简单网络管理协议）
reliable transfer over UDP:
  add reliability at application layer
  application-specific error recovery!

## Slide 18: UDP: segment header
source port #
dest port #
32 bits
application
data
(payload)
UDP segment format
length
checksum
length, in bytes of UDP segment, including header
no connection establishment (which can add delay)
simple: no connection state at sender, receiver
small header size
no congestion control: UDP can blast away as fast as desired
why is there a UDP?

## Slide 19: UDP checksum
sender:
treat segment contents, including header fields, as sequence of 16-bit integers
checksum: addition (one’s complement sum) of segment contents
sender puts checksum value into UDP checksum field
receiver:
compute checksum of received segment
check if computed checksum equals checksum field value:
  NO - error detected
  YES - no error detected. But maybe errors nonetheless? More later ….
Goal: detect “errors” (e.g., flipped bits) in transmitted segment

## Slide 20: Internet checksum: example
example: add two 16-bit integers
1 1 1 1 0 0 1 1 0 0 1 1 0 0 1 1 0
1 1 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 0 1 1
1 1 0 1 1 1 0 1 1 1 0 1 1 1 1 0 0
1 0 1 0 0 0 1 0 0 0 1 0 0 0 0 1 1
wraparound
sum
checksum
Note: when adding numbers, a carryout from the most significant bit needs to be added to the result
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/
Notes: Kurose and Ross forgot to say anything about wrapping the carry and adding it to low order bit

## Slide 21: Internet checksum: example
example: add two 16-bit integers
1 0 1 1 0 0 1 1 0 0 1 1 0 0 0 0 0
1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1
1 0 1 1 1 0 1 1 1 0 1 1 0 1 0 1
1 1 0 0 0 1 1 1 1 0 0 0 0 1 1 0 0
1 0 1 0 0 1 0 1 0 1 1 0 0 0 0 0 1
wraparound
sum
溢出的高位叠加到低位 -----》 后两位变成10
反码作为校验和
Notes: 发送方：原码相加 ，并将高位叠加到低位，取反 ，得到反码求和结果，放入校验和
接收方：将所有原码 相加，高位叠加， 如全为1，则正确

## Slide 22: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 23: Principles of reliable data transfer 可靠的数据传输
important in application, transport, link layers
  top-10 list of important networking topics!
characteristics of unreliable（不可靠） channel will determine complexity of reliable data transfer protocol (rdt)

## Slide 24: Principles of reliable data transfer
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)
important in application, transport, link layers
  top-10 list of important networking topics!

## Slide 25: Principles of reliable data transfer
characteristics of unreliable channel will determine complexity of reliable data transfer protocol (rdt)
important in application, transport, link layers
  top-10 list of important networking topics!

## Slide 26: Reliable data transfer: getting started
send
side
receive
side
rdt_send(): called from above, (e.g., by app.). Passed data to
deliver to receiver upper layer
udt_send(): called by rdt,
to transfer packet over
unreliable channel to receiver
rdt_rcv(): called when packet arrives on rcv-side of channel
deliver_data(): called by rdt to deliver data to upper

## Slide 27: Reliable data transfer: getting started
we’ll:
incrementally develop sender, receiver sides of reliable data transfer protocol (rdt)
consider only unidirectional data transfer
  but control info will flow on both directions!
use finite state machines (FSM，有限状态机) to specify sender, receiver
state
1
state
2
event causing state transition
actions taken on state transition
state: when in this “state” next state uniquely determined by next event
event
actions

## Slide 28: rdt1.0: reliable transfer over a reliable channel
underlying channel perfectly reliable
  no bit errors
  no loss of packets
separate FSMs for sender, receiver:
  sender sends data into underlying channel
  receiver reads data from underlying channel
Wait for call from above
packet = make_pkt(data)
udt_send(packet)
rdt_send(data)
extract (packet,data)
deliver_data(data)
Wait for call from below
rdt_rcv(packet)
sender
receiver

## Slide 29: rdt2.0: channel with bit errors
underlying channel may flip bits in packet
  checksum to detect bit errors
the question: how to recover from errors:
  acknowledgements (ACKs): receiver explicitly tells sender that pkt received OK
  negative acknowledgements (NAKs): receiver explicitly tells sender that pkt had errors
  sender retransmits pkt on receipt of NAK
new mechanisms in rdt2.0 (beyond rdt1.0):
  error detection
  receiver feedback: control msgs (ACK,NAK) rcvr->sender
How do humans recover from “errors”
during conversation?

## Slide 30: rdt2.0: channel with bit errors
underlying channel may flip bits in packet
  checksum to detect bit errors
the question: how to recover from errors:
  acknowledgements (ACKs): receiver explicitly tells sender that pkt received OK
  negative acknowledgements (NAKs): receiver explicitly tells sender that pkt had errors
  sender retransmits pkt on receipt of NAK
new mechanisms in rdt2.0 (beyond rdt1.0):
  error detection
  feedback: control msgs (ACK,NAK) from receiver to sender

## Slide 31: rdt2.0: FSM specification
Wait for call from above
sndpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
sender
receiver
rdt_send(data)
L

## Slide 32: rdt2.0: operation with no errors
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
L

## Slide 33: rdt2.0: error scenario
Wait for call from above
snkpkt = make_pkt(data, checksum)
udt_send(sndpkt)
extract(rcvpkt,data)
deliver_data(data)
udt_send(ACK)
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
rdt_rcv(rcvpkt) && isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
isNAK(rcvpkt)
udt_send(NAK)
rdt_rcv(rcvpkt) &&
corrupt(rcvpkt)
Wait for ACK or NAK
Wait for call from below
rdt_send(data)
L

## Slide 34: rdt2.0 has a fatal flaw! ACK/NAK会损坏
what happens if ACK/NAK corrupted?
sender doesn’t know what happened at receiver!
can’t just retransmit: possible duplicate
handling duplicates:
sender retransmits current pkt if ACK/NAK corrupted
sender adds sequence number to each pkt
receiver discards (doesn’t deliver up) duplicate pkt
stop and wait
sender sends one packet,
then waits for receiver
response

## Slide 35: rdt2.1: sender, handles garbled ACK/NAKs
Wait for call 0 from above
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
Wait for ACK or NAK 0
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isNAK(rcvpkt) )
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isNAK(rcvpkt) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt)
Wait for
call 1 from above
Wait for ACK or NAK 1
L
L

## Slide 36: rdt2.1: receiver, handles garbled ACK/NAKs
Wait for
0 from below
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq0(rcvpkt)
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
Wait for
1 from below
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq0(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
not corrupt(rcvpkt) &&
has_seq1(rcvpkt)
rdt_rcv(rcvpkt) && (corrupt(rcvpkt)
sndpkt = make_pkt(ACK, chksum)
udt_send(sndpkt)
sndpkt = make_pkt(NAK, chksum)
udt_send(sndpkt)
上面是之前的ACK可能出错了，发送方重发了0

## Slide 37: rdt2.1: discussion
sender:
seq # added to pkt
two seq. #’s (0,1) will suffice. Why?
must check if received ACK/NAK corrupted
twice as many states
  state must “remember” whether “expected” pkt should have seq # of 0 or 1
receiver:
must check if received packet is duplicate
  state indicates whether 0 or 1 is expected pkt seq #
note: receiver can not know if its last ACK/NAK received OK at sender

## Slide 38: rdt2.2: a NAK-free protocol
same functionality as rdt2.1, using ACKs only
instead of NAK, receiver sends ACK for last pkt received OK
  receiver must explicitly include seq # of pkt being ACKed
duplicate ACK at sender results in same action as NAK: retransmit current pkt

## Slide 39: rdt2.2: sender, receiver fragments
Wait for call 0 from above
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
rdt_send(data)
udt_send(sndpkt)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
Wait for ACK
0
sender FSM
fragment
rdt_rcv(rcvpkt) && notcorrupt(rcvpkt)
&& has_seq1(rcvpkt)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(ACK1, chksum)
udt_send(sndpkt)
Wait for
0 from below
rdt_rcv(rcvpkt) &&
(corrupt(rcvpkt) ||
has_seq1(rcvpkt))
sndpkt = make_pkt(ACK1, chksum)
udt_send(sndpkt)
receiver FSM
fragment
L

## Slide 40: rdt3.0: channels with errors and loss 从这里开始可能会丢包
new assumption: underlying channel can also lose packets (data, ACKs)
  checksum, seq. #, ACKs, retransmissions will be of help … but not enough
approach: sender waits “reasonable” amount of time for ACK
retransmits if no ACK received in this time
if pkt (or ACK) just delayed (not lost):
  retransmission will be duplicate, but seq. #’s already handles this
  receiver must specify seq # of pkt being ACKed
requires countdown timer

## Slide 41: rdt3.0 sender
sndpkt = make_pkt(0, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
Wait for ACK0
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,1) )
Wait for
call 1 from above
sndpkt = make_pkt(1, data, checksum)
udt_send(sndpkt)
start_timer
rdt_send(data)
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,0)
rdt_rcv(rcvpkt) &&
( corrupt(rcvpkt) ||
isACK(rcvpkt,0) )
rdt_rcv(rcvpkt)
&& notcorrupt(rcvpkt)
&& isACK(rcvpkt,1)
stop_timer
stop_timer
udt_send(sndpkt)
start_timer
timeout
udt_send(sndpkt)
start_timer
timeout
rdt_rcv(rcvpkt)
Wait for
call 0from above
Wait for ACK1
L
rdt_rcv(rcvpkt)
L
L
L

## Slide 42: rdt3.0 in action
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
pkt1
ack1
ack0
ack0
(a) no loss
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(b) packet loss
pkt1
X
loss
pkt1
timeout
resend pkt1

## Slide 43: rdt3.0 in action
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
rcv pkt0
send ack0
send ack1
send ack0
rcv ack0
send pkt0
send pkt1
rcv ack1
send pkt0
rcv pkt0
pkt0
pkt0
ack1
ack0
ack0
(c) ACK loss
ack1
X
loss
pkt1
timeout
resend pkt1
rcv pkt1
send ack1
(detect duplicate)
pkt1
sender
receiver
rcv pkt1
send ack0
rcv ack0
send pkt1
send pkt0
rcv pkt0
pkt0
ack0
(d) premature timeout/ delayed ACK
pkt1
timeout
resend pkt1
ack1
send ack1
send pkt0
rcv ack1
pkt0
ack1
ack0
send pkt0
rcv ack1
pkt0
rcv pkt0
send ack0
ack0
rcv pkt0
send ack0
(detect duplicate)

## Slide 44: Performance of rdt3.0
rdt3.0 is correct, but performance stinks
e.g.: 1 Gbps link, 15 ms prop. delay, 8000 bit packet:
  U sender: utilization – fraction of time sender busy sending
  if RTT=30 msec, 1KB pkt every 30 msec: 33kB/sec thruput over 1 Gbps link. RTT(Round-Trip Time) 往返时延
network protocol limits use of physical resources!
Dtrans =
L
R
8000 bits
109 bits/sec
=
=
8 microsecs
Notes: 万分之2.7
8us

## Slide 45: rdt3.0: stop-and-wait operation
first packet bit transmitted, t = 0
sender
receiver
RTT
last packet bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R

## Slide 46: Pipelined protocols
pipelining: sender allows multiple, “in-flight”, yet-to-be-acknowledged pkts
  range of sequence numbers must be increased
  buffering at sender and/or receiver
two generic forms of pipelined protocols: go-Back-N（回退n步）, selective repeat （选择重传）

## Slide 47: Pipelining: increased utilization
first packet bit transmitted, t = 0
sender
receiver
RTT
last bit transmitted, t = L / R
first packet bit arrives
last packet bit arrives, send ACK
ACK arrives, send next
packet, t = RTT + L / R
last bit of 2nd packet arrives, send ACK
last bit of 3rd packet arrives, send ACK
3-packet pipelining increases
utilization by a factor of 3!

## Slide 48: Pipelined protocols: overview
Go-back-N:
sender can have up to N unacked packets in pipeline
receiver only sends cumulative ack（累积确认）
  doesn’t ack packet if there’s a gap
sender has timer for oldest unacked packet
  when timer expires, retransmit all unacked packets
Selective Repeat:
sender can have up to N unack’ed packets in pipeline
rcvr sends individual ack for each packet
sender maintains timer for each unacked packet
  when timer expires, retransmit only that unacked packet

## Slide 49: Go-Back-N: sender
k-bit seq # in pkt header
“window” of up to N, consecutive unack’ed pkts allowed
ACK(n): ACKs all pkts up to, including seq # n - “cumulative ACK” 累积确认
  may receive duplicate ACKs (see receiver)
timer for oldest in-flight pkt
timeout(n): retransmit packet n and all higher seq # pkts in window

## Slide 50: GBN: sender extended FSM
Wait
start_timer
udt_send(sndpkt[base])
udt_send(sndpkt[base+1])
…
udt_send(sndpkt[nextseqnum-1])
timeout
rdt_send(data)
if (nextseqnum < base+N) {
sndpkt[nextseqnum] = make_pkt(nextseqnum,data,chksum)
udt_send(sndpkt[nextseqnum])
if (base == nextseqnum)
start_timer
nextseqnum++
}
else
refuse_data(data)
base = getacknum(rcvpkt)+1
If (base == nextseqnum)
stop_timer
else
start_timer
rdt_rcv(rcvpkt) &&
notcorrupt(rcvpkt)
base=1
nextseqnum=1
rdt_rcv(rcvpkt)
&& corrupt(rcvpkt)
L
最早的已发送未确认启动定时器
没有已发送未确认的分组
窗口未满

## Slide 51: GBN: receiver extended FSM
ACK-only: always send ACK for correctly-received pkt with highest in-order seq #
  may generate duplicate ACKs
  need only remember expectedseqnum
out-of-order pkt:
  discard (don’t buffer): no receiver buffering!
  re-ACK pkt with highest in-order seq #
Wait
udt_send(sndpkt)
default
rdt_rcv(rcvpkt)
&& notcurrupt(rcvpkt)
&& hasseqnum(rcvpkt,expectedseqnum)
extract(rcvpkt,data)
deliver_data(data)
sndpkt = make_pkt(expectedseqnum,ACK,chksum)
udt_send(sndpkt)
expectedseqnum++
expectedseqnum=1
sndpkt =
make_pkt(expectedseqnum,ACK,chksum)
L
其它情况
丢弃，重新发相同的ack

## Slide 52: GBN in action
send pkt0
send pkt1
send pkt2
send pkt3
(wait)
sender
receiver
receive pkt0, send ack0
receive pkt1, send ack1
receive pkt3, discard,
(re)send ack1
rcv ack0, send pkt4
rcv ack1, send pkt5
pkt 2 timeout
send pkt2
send pkt3
send pkt4
send pkt5
X
loss
receive pkt4, discard,
(re)send ack1
receive pkt5, discard,
(re)send ack1
rcv pkt2, deliver, send ack2
rcv pkt3, deliver, send ack3
rcv pkt4, deliver, send ack4
rcv pkt5, deliver, send ack5
ignore duplicate ACK
0 1 2 3 4 5 6 7 8
sender window (N=4)
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8

## Slide 53: Selective repeat（选择重传）
receiver individually acknowledges all correctly received pkts
  buffers pkts, as needed, for eventual in-order delivery to upper layer
sender only resends pkts for which ACK not received
  sender timer for each unACKed pkt
sender window
  N consecutive seq #’s
  limits seq #s of sent, unACKed pkts

## Slide 54: Selective repeat: sender, receiver windows

## Slide 55: Selective repeat
data from above:
if next available seq # in window, send pkt
timeout(n):
resend pkt n, restart timer
ACK(n) in [sendbase,sendbase+N]:
mark pkt n as received
if n smallest unACKed pkt, advance window base to next unACKed seq #
sender
pkt n in [rcvbase, rcvbase+N-1]
send ACK(n)
out-of-order: buffer
in-order: deliver (also deliver buffered, in-order pkts), advance window to next not-yet-received pkt
pkt n in [rcvbase-N,rcvbase-1]
ACK(n)
otherwise:
ignore
receiver

## Slide 56: Selective repeat in action
send pkt0
send pkt1
send pkt2
send pkt3
(wait)
sender
receiver
receive pkt0, send ack0
receive pkt1, send ack1
receive pkt3, buffer,
send ack3
rcv ack0, send pkt4
rcv ack1, send pkt5
pkt 2 timeout
send pkt2
X
loss
receive pkt4, buffer,
send ack4
receive pkt5, buffer,
send ack5
rcv pkt2; deliver pkt2,
pkt3, pkt4, pkt5; send ack2
record ack3 arrived
0 1 2 3 4 5 6 7 8
sender window (N=4)
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
0 1 2 3 4 5 6 7 8
record ack4 arrived
record ack5 arrived
Q: what happens when ack2 arrives?

## Slide 57: Selective repeat: dilemma
example:
seq #’s: 0, 1, 2, 3
window size=3
receiver window
(after receipt)
sender window
(after receipt)
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
timeout
retransmit pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
X
X
will accept packet
with seq number 0
(b) oops!
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
pkt0
pkt1
pkt2
0 1 2 3 0 1 2
pkt0
0 1 2 3 0 1 2
0 1 2 3 0 1 2
0 1 2 3 0 1 2
X
will accept packet
with seq number 0
0 1 2 3 0 1 2
pkt3
(a) no problem
receiver can’t see sender side.
receiver behavior identical in both cases!
something’s (very) wrong!
receiver sees no difference in two scenarios!
duplicate data accepted as new in (b)
Q: what relationship between seq # size and window size to avoid problem in (b)?

## Slide 58: 作业
将rdt 2.2补充完整
画出rdt 3.0接收端的FSM图。
说明窗口大小和序号空间大小的关系，并解释原因。
窗口小于等于序号空间的一半 N/2 (SR)
窗口小于等于N-1 (GBN)

## Slide 59: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 60: TCP: Overview RFCs: 793,1122,1323, 2018, 2581
full duplex data:
  bi-directional（双工） data flow in same connection
  MSS: maximum segment size 最大报文段长度
connection-oriented:
  handshaking (exchange of control msgs) inits sender, receiver state before data exchange
flow controlled:
  sender will not overwhelm receiver
point-to-point:
  one sender, one receiver
reliable, in-order byte stream:
  no “message boundaries”
pipelined:
  TCP congestion and flow control set window size
Notes: 逻辑连接，共同状态仅仅保留在两个端系统的TCP程序中。
TCP协议只在端系统中运行。重点的网络元素不会维持TCP的连接状态。中间路由器对TCP连接完全视而不见，他们看到的是数据报，而不是连接。
三次握手协商一些参数，比如发送缓存。
最大报文段MSS，最大链路层帧长度MTU
MSS是应用层长度

## Slide 61: TCP segment structure
source port #
dest port #
32 bits
application
data
(variable length)
sequence number
acknowledgement number
receive window
Urg data pointer
checksum
F
S
R
P
A
U
head
len
not
used
options (variable length)
URG: urgent data
(generally not used)
ACK: ACK #
valid
PSH: push data now
(generally not used)
RST, SYN, FIN:
connection estab
(setup, teardown
commands)
# bytes
rcvr willing
to accept
counting
by bytes
of data
(not segments!)
Internet
checksum
(as in UDP)

## Slide 62: TCP seq. numbers, ACKs
sequence numbers:（序号）
  byte stream “number” of first byte in segment’s data
acknowledgements:（确认号）seq # of next byte expected from other side
  cumulative ACK
Q: how receiver handles out-of-order segments
  A: TCP spec doesn’t say, - up to implementor
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
urg pointer
incoming segment to sender
A
sent
ACKed
sent, not-yet ACKed
(“in-flight”)
usable
but not
yet sent
not
usable
window size
N
  sender sequence number space
source port #
dest port #
sequence number
acknowledgement number
checksum
rwnd
urg pointer
outgoing segment from sender
Notes: 序号是字节流的编号

## Slide 63: TCP seq. numbers, ACKs
User
types
‘C’
host ACKs
receipt
of echoed
‘C’
host ACKs
receipt of
‘C’, echoes
back ‘C’
simple telnet scenario
Host B
Host A
Seq=42, ACK=79, data = ‘C’
Seq=79, ACK=43, data = ‘C’
Seq=43, ACK=80
Notes: 累积确认。
随机选择序列号。

## Slide 64: TCP round trip time, timeout
Q: how to set TCP timeout value?
longer than RTT
  but RTT varies
too short: premature timeout, unnecessary retransmissions
too long: slow reaction to segment loss
Q: how to estimate RTT?
SampleRTT: measured time from segment transmission until ACK receipt
  ignore retransmissions
SampleRTT will vary, want estimated RTT “smoother”
  average several recent measurements, not just current SampleRTT

## Slide 65: TCP round trip time, timeout
EstimatedRTT = (1- )*EstimatedRTT + *SampleRTT
exponential weighted moving average（指数加权移动平均）
influence of past sample decreases exponentially fast
typical value:  = 0.125
RTT (milliseconds)
RTT: gaia.cs.umass.edu to fantasia.eurecom.fr
sampleRTT
EstimatedRTT
time (seconds)

## Slide 66: TCP round trip time, timeout
timeout interval: EstimatedRTT plus “safety margin”
  large variation in EstimatedRTT -> larger safety margin
estimate SampleRTT deviation（偏差） from EstimatedRTT:
DevRTT = (1-)*DevRTT +
*|SampleRTT-EstimatedRTT|
(typically,  = 0.25)
TimeoutInterval = EstimatedRTT + 4*DevRTT
estimated RTT
“safety margin”
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 67: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 68: TCP reliable data transfer
TCP creates rdt service on top of IP’s unreliable service
  pipelined segments
  cumulative acks
  single retransmission timer
retransmissions triggered by:
  timeout events
  duplicate acks
let’s initially consider simplified TCP sender:
  ignore duplicate acks
  ignore flow control, congestion control

## Slide 69: TCP sender events:
data rcvd from app:
create segment with seq #
seq # is byte-stream number of first data byte in segment
start timer if not already running
  think of timer as for oldest unacked segment
  expiration interval: TimeOutInterval
timeout:
retransmit segment that caused timeout
restart timer
ack rcvd:
if ack acknowledges previously unacked segments
  update what is known to be ACKed
  start timer if there are still unacked segments

## Slide 70: TCP sender (simplified)
wait
for
event
NextSeqNum = InitialSeqNum
SendBase = InitialSeqNum
L
create segment, seq. #: NextSeqNum
pass segment to IP (i.e., “send”)
NextSeqNum = NextSeqNum + length(data)
if (timer currently not running)
start timer
data received from application above
retransmit not-yet-acked segment with smallest seq. #
start timer
timeout
if (y > SendBase) {
SendBase = y
/* SendBase–1: last cumulatively ACKed byte */
if (there are currently not-yet-acked segments)
start timer
else stop timer
}
ACK received, with ACK field value y

## Slide 71: TCP: retransmission scenarios
lost ACK scenario
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
Seq=92, 8 bytes of data
X
timeout
ACK=100
premature timeout
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
Seq=92, 8
bytes of data
timeout
ACK=120
Seq=100, 20 bytes of data
ACK=120
SendBase=100
SendBase=120
SendBase=120
SendBase=92

## Slide 72: TCP: retransmission scenarios
X
cumulative ACK
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
Seq=120, 15 bytes of data
timeout
Seq=100, 20 bytes of data
ACK=120

## Slide 73: TCP ACK generation [RFC 1122, RFC 2581]
event at receiver
arrival of in-order segment with
expected seq #. All data up to
expected seq # already ACKed
arrival of in-order segment with
expected seq #. One other
segment has ACK pending
arrival of out-of-order segment
higher-than-expect seq. # .
Gap detected
arrival of segment that
partially or completely fills gap
TCP receiver action
delayed ACK. Wait up to 500ms
for next segment. If no next segment,
send ACK
immediately send single cumulative
ACK, ACKing both in-order segments
immediately send duplicate ACK,
indicating seq. # of next expected byte
immediate send ACK, provided that
segment starts at lower end of gap

## Slide 74: TCP fast retransmit
time-out period often relatively long:
  long delay before resending lost packet
detect lost segments via duplicate ACKs.
  sender often sends many segments back-to-back
  if segment is lost, there will likely be many duplicate ACKs.
if sender receives 3 ACKs for same data
(“triple duplicate ACKs”), resend unacked segment with smallest seq #
  likely that unacked segment lost, so don’t wait for timeout
TCP fast retransmit
(“triple duplicate ACKs”),

## Slide 75: TCP fast retransmit
X
fast retransmit after sender
receipt of triple duplicate ACK
Host B
Host A
Seq=92, 8 bytes of data
ACK=100
timeout
ACK=100
ACK=100
ACK=100
Seq=100, 20 bytes of data
Seq=100, 20 bytes of data

## Slide 76: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 77: TCP flow control
application
process
TCP socket
receiver buffers
TCP
code
IP
code
application
OS
receiver protocol stack
application may
remove data from
TCP socket buffers ….
… slower than TCP
receiver is delivering
(sender is sending)
from sender
receiver controls sender, so sender won’t overflow receiver’s buffer by transmitting too much, too fast
flow control

## Slide 78: TCP flow control
buffered data
free buffer space
rwnd
RcvBuffer
TCP segment payloads
to application process
receiver “advertises” free buffer space by including rwnd value in TCP header of receiver-to-sender segments
  RcvBuffer size set via socket options (typical default is 4096 bytes)
  many operating systems autoadjust RcvBuffer
sender limits amount of unacked (“in-flight”) data to receiver’s rwnd value
guarantees receive buffer will not overflow
receiver-side buffering

## Slide 79: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 80: Connection Management
before exchanging data, sender/receiver “handshake”:
agree to establish connection (each knowing the other willing to establish connection)
agree on connection parameters
connection state: ESTAB
connection variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
connection state: ESTAB
connection Variables:
  seq # client-to-server
  server-to-client
  rcvBuffer size
  at server,client
application
network
Socket clientSocket =
newSocket("hostname","port number");
Socket connectionSocket = welcomeSocket.accept();

## Slide 81: Agreeing to establish a connection
Q: will 2-way handshake always work in network?
variable delays
retransmitted messages (e.g. req_conn(x)) due to message loss
message reordering
can’t “see” other side
2-way handshake:
Let’s talk
OK
ESTAB
ESTAB
choose x
req_conn(x)
ESTAB
ESTAB
acc_conn(x)

## Slide 82: TCP 3-way handshake
SYNbit=1, Seq=x
choose init seq num, x
send TCP SYN msg
ESTAB
SYNbit=1, Seq=y
ACKbit=1; ACKnum=x+1
choose init seq num, y
send TCP SYNACK
msg, acking SYN
ACKbit=1, ACKnum=y+1
received SYNACK(x)
indicates server is live;
send ACK for SYNACK;
this segment may contain
client-to-server data
received ACK(y)
indicates client is live
SYNSENT
ESTAB
SYN RCVD
client state
LISTEN
server state
LISTEN
Notes: TCP 协议规定SYN报文虽然不携带数据， 但是也要消耗1个序列号， 所以前两次握手客户端和服务端都需要向对方回复 x+1 或 y+1 。
https://blog.csdn.net/lengxiao1993/article/details/82771768

## Slide 83: TCP 3-way handshake: FSM
closed
L
listen
SYN
rcvd
SYN
sent
ESTAB
Socket clientSocket =
newSocket("hostname","port number");
SYN(seq=x)
Socket connectionSocket = welcomeSocket.accept();
SYN(x)
SYNACK(seq=y,ACKnum=x+1)
create new socket for
communication back to client
SYNACK(seq=y,ACKnum=x+1)
ACK(ACKnum=y+1)
ACK(ACKnum=y+1)
L
Notes: 图的右边是客户端，左边是服务器。

## Slide 84: TCP: closing a connection
client, server each close their side of connection
  send TCP segment with FIN bit = 1
respond to received FIN with ACK
  on receiving FIN, ACK can be combined with own FIN
simultaneous FIN exchanges can be handled

## Slide 85: TCP: closing a connection
FIN_WAIT_2
CLOSE_WAIT
FINbit=1, seq=y
ACKbit=1; ACKnum=y+1
ACKbit=1; ACKnum=x+1
wait for server
close
can still
send data
can no longer
send data
LAST_ACK
CLOSED
TIMED_WAIT
timed wait
for 2*max
segment lifetime
CLOSED
FIN_WAIT_1
FINbit=1, seq=x
can no longer
send but can
receive data
clientSocket.close()
client state
server state
ESTAB
ESTAB

## Slide 86: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 87: 拥塞控制
为什么会产生拥塞？
跟流量控制有什么不一样？
TCP有什么方法控制拥塞？
怎么发现拥塞？
如何避免？
如何恢复？

## Slide 88: Principles of congestion control
congestion:
informally: “too many sources sending too much data too fast for network to handle”
different from flow control!
manifestations:
  lost packets (buffer overflow at routers)
  long delays (queueing in router buffers)
a top-10 problem!

## Slide 89: Causes/costs of congestion: scenario 1
two senders, two receivers
one router, infinite buffers
output link capacity: R
no retransmission
maximum per-connection throughput: R/2
unlimited shared output link buffers
Host A
original data: lin
Host B
throughput: lout
R/2
R/2
lout
lin
R/2
delay
lin
large delays as arrival rate, lin, approaches capacity

## Slide 90: Causes/costs of congestion: scenario 2
one router, finite buffers
sender retransmission of timed-out packet
  application-layer input = application-layer output: lin = lout
  transport-layer input includes retransmissions : lin lin
finite shared output link buffers
Host A
lin : original data
Host B
lout
l'in: original data, plus retransmitted data
‘

## Slide 91: Causes/costs of congestion: scenario 2
idealization: perfect knowledge
sender sends only when router buffers available
finite shared output link buffers
lin : original data
lout
l'in: original data, plus retransmitted data
copy
free buffer space!
R/2
R/2
lout
lin
Host B
A

## Slide 92: Causes/costs of congestion: scenario 2
lin : original data
lout
l'in: original data, plus retransmitted data
copy
no buffer space!
Idealization: known loss packets can be lost, dropped at router due to full buffers
sender only resends if packet known to be lost
A
Host B

## Slide 93: Causes/costs of congestion: scenario 2
lin : original data
lout
l'in: original data, plus retransmitted data
free buffer space!
Idealization: known loss packets can be lost, dropped at router due to full buffers
sender only resends if packet known to be lost
R/2
R/2
lin
lout
when sending at R/2, some packets are retransmissions but asymptotic goodput is still R/2 (why?)
A
Host B

## Slide 94: Causes/costs of congestion: scenario 2
A
lin
lout
l'in
copy
free buffer space!
timeout
R/2
R/2
lin
lout
when sending at R/2, some packets are retransmissions including duplicated that are delivered!
Host B
Realistic: duplicates
packets can be lost, dropped at router due to full buffers
sender times out prematurely, sending two copies, both of which are delivered

## Slide 95: Causes/costs of congestion: scenario 2
R/2
lout
when sending at R/2, some packets are retransmissions including duplicated that are delivered!
“costs” of congestion:
more work (retrans) for given “goodput”
unneeded retransmissions: link carries multiple copies of pkt
  decreasing goodput
R/2
lin
Realistic: duplicates
packets can be lost, dropped at router due to full buffers
sender times out prematurely, sending two copies, both of which are delivered

## Slide 96: Causes/costs of congestion: scenario 3
four senders
multihop paths
timeout/retransmit
Q: what happens as lin and lin’ increase ?
finite shared output link buffers
Host A
lout
Host B
Host C
Host D
lin : original data
l'in: original data, plus retransmitted data
A: as red lin’ increases, all arriving blue pkts at upper queue are dropped, blue throughput g 0

## Slide 97: Causes/costs of congestion: scenario 3
another “cost” of congestion:
when packet dropped, any “upstream transmission capacity used for that packet was wasted!
C/2
C/2
lout
lin’

## Slide 98: Chapter 3 outline
3.1 transport-layer services
3.2 multiplexing and demultiplexing
3.3 connectionless transport: UDP
3.4 principles of reliable data transfer
3.5 connection-oriented transport: TCP
  segment structure
  reliable data transfer
  flow control
  connection management
3.6 principles of congestion control
3.7 TCP congestion control

## Slide 99: TCP congestion control: additive increase multiplicative decrease
approach: sender increases transmission rate (window size), probing for usable bandwidth, until loss occurs
  additive increase: increase cwnd by 1 MSS every RTT until loss detected
  multiplicative decrease: cut cwnd in half after loss
cwnd: TCP sender
congestion window size
AIMD saw tooth
behavior: probing
for bandwidth
additively increase window size …
…. until loss occurs (then cut window in half)
time

## Slide 100: TCP Congestion Control: details
sender limits transmission:
cwnd is dynamic, function of perceived network congestion
TCP sending rate:
roughly: send cwnd bytes, wait RTT for ACKS, then send more bytes
last byte
ACKed
sent, not-yet ACKed
(“in-flight”)
last byte sent
cwnd
LastByteSent-
LastByteAcked
<
cwnd
sender sequence number space
rate
~
~
cwnd
RTT
bytes/sec

## Slide 101: TCP Slow Start
when connection begins, increase rate exponentially until first loss event:
  initially cwnd = 1 MSS
  double cwnd every RTT
  done by incrementing cwnd for every ACK received
summary: initial rate is slow but ramps up exponentially fast
Host A
one segment
RTT
Host B
time
two segments
four segments

## Slide 102: TCP: detecting, reacting to loss
loss indicated by timeout:
  cwnd set to 1 MSS;
  window then grows exponentially (as in slow start) to threshold, then grows linearly
loss indicated by 3 duplicate ACKs: TCP RENO
  dup ACKs indicate network capable of delivering some segments
  cwnd is cut in half window then grows linearly
TCP Tahoe always sets cwnd to 1 (timeout or 3 duplicate acks)

## Slide 103: TCP: switching from slow start to CA
Q: when should the exponential increase switch to linear?
A: when cwnd gets to 1/2 of its value before timeout.
Implementation:
variable ssthresh
on loss event, ssthresh is set to 1/2 of cwnd just before loss event
* Check out the online interactive exercises for more examples: http://gaia.cs.umass.edu/kurose_ross/interactive/

## Slide 104: Summary: TCP Congestion Control
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
L
cwnd > ssthresh
congestion
avoidance
cwnd = cwnd + MSS (MSS/cwnd)
dupACKcount = 0
transmit new segment(s), as allowed
new ACK
.
dupACKcount++
duplicate ACK
fast
recovery
cwnd = cwnd + MSS
transmit new segment(s), as allowed
duplicate ACK
ssthresh= cwnd/2
cwnd = ssthresh + 3
retransmit missing segment
dupACKcount == 3
timeout
ssthresh = cwnd/2
cwnd = 1
dupACKcount = 0
retransmit missing segment
ssthresh= cwnd/2
cwnd = ssthresh + 3
retransmit missing segment
dupACKcount == 3
cwnd = ssthresh
dupACKcount = 0
New ACK
slow
start
timeout
ssthresh = cwnd/2
cwnd = 1 MSS
dupACKcount = 0
retransmit missing segment
cwnd = cwnd+MSS
dupACKcount = 0
transmit new segment(s), as allowed
new ACK
dupACKcount++
duplicate ACK
L
cwnd = 1 MSS
ssthresh = 64 KB
dupACKcount = 0
New
ACK!
New
ACK!
New
ACK!

## Slide 105: TCP throughput
avg. TCP thruput as function of window size, RTT?
  ignore slow start, assume always data to send
W: window size (measured in bytes) where loss occurs
  avg. window size (# in-flight bytes) is ¾ W
  avg. thruput is 3/4W per RTT
W
W/2
avg TCP thruput =
3
4
W
RTT
bytes/sec

## Slide 106: TCP Futures: TCP over “long, fat pipes”
example: 1500 byte segments, 100ms RTT, want 10 Gbps throughput
requires W = 83,333 in-flight segments
throughput in terms of segment loss probability, L [Mathis 1997]:
  ➜ to achieve 10 Gbps throughput, need a loss rate of L = 2·10-10 – a very small loss rate!
new versions of TCP for high-speed
TCP throughput =
1.22
.
MSS
RTT
L

## Slide 107: TCP Fairness
fairness goal: if K TCP sessions share same bottleneck link of bandwidth R, each should have average rate of R/K
TCP connection 1
bottleneck
router
capacity R
TCP connection 2

## Slide 108: Why is TCP fair?
two competing sessions:
additive increase gives slope of 1, as throughout increases
multiplicative decrease decreases throughput proportionally
R
R
equal bandwidth share
Connection 1 throughput
Connection 2 throughput
congestion avoidance: additive increase
loss: decrease window by factor of 2
congestion avoidance: additive increase
loss: decrease window by factor of 2

## Slide 109: Fairness (more)
Fairness and UDP
multimedia apps often do not use TCP
  do not want rate throttled by congestion control
instead use UDP:
  send audio/video at constant rate, tolerate packet loss
Fairness, parallel TCP connections
application can open multiple parallel connections between two hosts
web browsers do this
e.g., link of rate R with 9 existing connections:
  new app asks for 1 TCP, gets rate R/10
  new app asks for 11 TCPs, gets R/2

## Slide 110: Explicit Congestion Notification (ECN)
network-assisted congestion control:
two bits in IP header (ToS field) marked by network router to indicate congestion
congestion indication carried to receiving host
receiver (seeing congestion indication in IP datagram) ) sets ECE bit on receiver-to-sender ACK segment to notify sender of congestion
source
application
transport
network
link
physical
destination
application
transport
network
link
physical
ECN=11
ECN=00
ECN=11
ECE=1
IP datagram
TCP ACK segment

## Slide 111: Chapter 3: summary
principles behind transport layer services:
  multiplexing, demultiplexing
  reliable data transfer
  flow control
  congestion control
instantiation, implementation in the Internet
  UDP
  TCP
next:
leaving the network “edge” (application, transport layers)
into the network “core”
two network layer chapters:
  data plane
  control plane